Renewable Sources of Energy				7En 6c (answers n/c)

| Source of energy | How it works | Benefits | Problems |
| --- | --- | --- | --- |
| Biofuels | Plants (especially fast growing trees) can be grown to burn as fuels. Rotting plants & manure can make methane gas | Plants are renewable – you can grow some more. It uses up natural waste products | Burning ANY fuels releases carbon dioxide (a greenhouse gas) and pollution. |
| Solar Cells | Solar cells transfer some of the sun’s energy into electricity. Solar panels use the heat from the sun to heat water. | The Suns energy is freely available whenever it shines. It won’t run out! Solar panels provide cheap hot water. | Solar cells are expensive and can’t provide large amounts of electricity. Doesn’t work at night and only a bit on dull days. |
| Geothermal | Water in the ground can be heated by hot rocks deep in the earth. | Available free, day and night. | Only possible where the earths crust is thin and the rocks are hot near the surface (e.g. geysers) |
| Hydro-electric | Water from rivers is stored behind dams. It can then run down pipes to turn generators to make electricity. | Whenever it rains the dams are refilled. Can make huge amounts of electricity. | Can only be made in hilly valleys. Floods large areas of land. |
| Tidal | Huge dams harness the power of the tides to turn turbines to generate electricity. | The tides never stop. Can make huge amounts of electricity. | Only a few places in the world have very high tides & estuaries. |
| Wind | Giant turbines are turned by the wind to generate electricity | Whenever the wind blows we get free electricity. | Doesn’t work when the wind stops or is too fast. Many generators are needed to make a lot of electricity. |